## Slide 1
Turn it up to
save energy
Charlotte Winnert – Environment & IMS Manager
Louis Garnham – Environmental Assistant

## Slide 2
Contents
Context and background
  University of Sheffield: environmental impact and net zero carbon goals
  Understanding carbon emissions
The environmental impact of our research
Investigating the environmental impact of ULT freezers
https://www.sheffield.ac.uk/sustainability

## Slide 3
https://www.sheffield.ac.uk/sustainability
The scale of our environmental impact
Notes: 121,000?

## Slide 4
In 2018/19 our activities were responsible for an estimated 121,000 tonnes of carbon emissions…
… while the average UK household is estimated
to be responsible for 8 tonnes of carbon annually
https://www.sheffield.ac.uk/sustainability
The scale of our environmental impact
Notes: 121,000?

## Slide 5
The University aims to become one of the most sustainable research-intensive universities in the country and we will align our research, teaching and campus to ensure sustainable practice across everything we do.
We are committed to becoming net carbon neutral on campus by 2030 and across all activities by 2038.
https://www.sheffield.ac.uk/sustainability
Our commitments
Notes: 121,000?

## Slide 6
https://www.sheffield.ac.uk/sustainability
Understanding carbon emissions
Types of carbon emissions:
Scope 1 – direct emissions from our owned or controlled sources
→ e.g., boilers and vehicles
Scope 2 – indirect emissions from purchased energy
→ e.g., heating and cooling buildings, running equipment
Scope 3 – Indirect emissions from an organisation’s supply chain
→ e.g., the manufacture, shipping, and disposal of all materials & resources
Becoming net carbon neutral requires reducing emissions across all scopes.

## Slide 7
https://www.sheffield.ac.uk/sustainability
The impact of our research

## Slide 8
https://www.sheffield.ac.uk/sustainability
The impact of our research
In 2018/19 our institutional carbon emissions totalled 121,182 tonnes CO2e.
Our scientific research was responsible for just under 50% of these emissions whilst occupying just 7% of our floor space.
Area | Costs | Estimated gross tonnes CO2e | Emission category
Consumables & materials | £22,900,000 | 59,105 | Scope 3
Energy | £2,300,000 | 4,100 | Scopes 1 & 2
Water | £450,000 | 17 | Scope 3
Waste disposal | £75,000 | 29 | Scope 3
Total | £25,725,000 | 63,251 | 
Estimated costs & carbon emissions from our research (2018/19)
Notes: 121,000?

## Slide 9
https://www.sheffield.ac.uk/sustainability
The impact of our research
In 2018/19 our institutional carbon emissions totalled 121,182 tonnes CO2e.
Our scientific research was responsible for just under 50% of these emissions whilst occupying just 7% of our floor space.
Area | Costs | Estimated gross tonnes CO2e | Emission category
Consumables & materials | £22,900,000 | 59,105 | Scope 3
Energy | £2,300,000 | 4,100 | Scopes 1 & 2
Water | £450,000 | 17 | Scope 3
Waste disposal | £75,000 | 29 | Scope 3
Total | £25,725,000 | 63,251 | 
Estimated costs & carbon emissions from our research (2018/19)
Notes: 121,000?

## Slide 10
Decarbonisation Strategy (2023), core principle #3 → “Demand reduction lessens the burden”
https://www.sheffield.ac.uk/sustainability
The impact of our research
Area | Costs | Estimated gross tonnes CO2e | Emission category
Consumables & materials | £22,900,000 | 59,105 | Scope 3
Energy | £2,300,000 | 4,100 | Scopes 1 & 2
Water | £450,000 | 17 | Scope 3
Waste disposal | £75,000 | 29 | Scope 3
Total | £25,725,000 | 63,251 | 
Estimated costs & carbon emissions from our research (2018/19)
Notes: 121,000?

## Slide 11
ULT freezers are energy intensive!
New: 7 kWh/day =
Up to ~35 kWh/day - range of factors, primarily age
Nearly 200 at Uni of Sheffield
Large impact - but how large? How to reduce impact? What £/CO2 savings can be made?
https://www.sheffield.ac.uk/sustainability
Ultra-low temperature freezers

## Slide 12
School of Biosciences: ~85 ULT freezers
How are they used?
User requirements
Energy consumption
How to reduce energy consumption → environmental impact?
Answers from conversations, freezer audits, energy monitoring
https://www.sheffield.ac.uk/sustainability
Project approach

## Slide 13
Avg energy consumption 12–20 kWh/day /unit
  Excluding extra heat load on air conditioning!
Opportunities to reduce energy consumption by 30+% whilst reducing risks in research
https://www.sheffield.ac.uk/sustainability
Findings
Energy (year) | Gross emissions | £ 2023/24
372,000–620,000 kWh | 72–120 tCO2e | £113,900–£189,800

## Slide 14
Currently: ~90% freezers at -80°C, handful at -70°C
-80° → -70° energy saving 15-40%
-80° → -60° energy saving 40+% (backups)
-70°C is big topic in sustainable science
  online database of samples being stored at -70
  institutions below running many/all freezers at -70
  Roslin Institute: long term study of sample preservation
Findings and recommendations: set temperature
Action | Energy (year) | Gross emissions | £ 2023/24
53 freezers (70%) to -70°C | 62,000 kWh | 12 tonnes CO2e | £18,900
All 8 backups to -60°C | 16,000 kWh | 3 tonnes CO2e | £4,900
Credit: Anna Albecka-Moreau, Twitter

## Slide 15
Lack of / poor inventory
  harder to find samples
  door open longer → temp fluctuations
→ buildup of snow and ice
→ compressor wear & tear
→ door not closing properly
Not using racks
  these aid organisation and protects samples from temp fluctuations
Dust and ice
  compressor overworked, high energy consumption, wear & tear
Action: implement better organisation and preventative maintenance
→ inventories, racks, clearouts, de-icing, filter cleaning
Direct savings not easy to quantify - but actions still helpful
https://www.sheffield.ac.uk/sustainability
Findings and recommendations: organisation & housekeeping

## Slide 16
Currently: most freezers not full, not shared
Free up more space with clearouts and better organisation
Consolidate into fewer units, turn old freezers off (standby)
Findings and recommendations: consolidation
Action | Energy (year) | Gross emissions | £ 2023/24
Switch off 5 old freezers (25 kWh/d) | 45,600 kWh | 8.8 tonnes CO2e | £14,000
https://www.sheffield.ac.uk/sustainability

## Slide 17
Uni of Sheffield: net carbon neutral by 2030 for scopes 1 & 2; all scopes by 2038
Scientific research: ~50% of campus emissions, 7% of floor space
  environmental impact of research must be addressed
We all need to contribute to help reach net zero
Decarbonisation strategy → reduce energy demand
Ultralow freezers - found opportunities to reduce energy use and provide benefits to users
Have a look at your labs!
Summary
https://www.sheffield.ac.uk/sustainability